## Slide 1
DVP 10MC System Architecture
WJ Solution center
2012. Aug. 25

## Slide 2: Content
1. Preparation
2. Software Communication Port
3. Motion Control Network Configuration
4. Downloading of Network Configuration and Program
5. Motion Control Function Planning
6. On-line Monitoring of Motion Control Program
7. Diagnosis of LED and Debugging

## Slide 3: Preparation
: Software
: Servo parameters setting:
P1-01=0B: Set A2 servo to CANopen mode
P3-00=1: Set node ID of A2 servo to “1”
P3-01=403: The baud rate of A2 servo in CANopen network is set to 1Mbps
P2-15=122: Set the parameter to “NO” (normally open)
P2-16=123: Set the parameter to “NO” (normally open)
P2-17=121: Set the parameter to “NO” (normally open)
Download CANopen Builder software from
Delta website and then install it.
: Hardware and structure figure
One DVP10MC11T
Two resistors (TAP-TR01)
One CANopen communication cable (TAP-CB03 or TAP-CB05/CB10)
One HMI
One Ethernet cable
One A2 servo

## Slide 4: Setup of Communication Port(1)
4
Method of connecting computer to the Ethernet port of DVP10MC11T
Steps for setting Ethernet software
Open CANopen Builder software interface
Click “Setup”-> “Communication setting”-> “Ethernet channel” in the menu.
Enter “Ethernet Setting” interface
2. Connect via the network switchboard
1. Connect via cable
Internet
Switchboard

## Slide 5: Setup of Communication Port(2)
5
6. Then “Ethernet Config” dialog box appears.
4. Click “Broadcast Search” and the searched DVP10MC11T will show in “Ethernet setting” dialog box. Afterwards, click “Setup…” button.
5. Then the “Input Password” dialog box pops up, input the password there and then click “OK”.

## Slide 6: Setup of Communication Port(3)
Explanation of Ethernet parameters:
8. The appearing of success of “CANopen Builder” indicates that the parameters setting is correct.
7. Set the appropriate parameters in “Ethernet Config” dialog box. (Select “Static” for IP Configuration in the example) And then click “OK”.
Name | Device name ( You can name it by yourself）
IP address | IP address of DVP10MC11T
IP type | IP configuration of DVP10MC11T can be DHCP or Static. If “DHCP” is selected, the Ethernet parameters are acquired by DVP10MC11T itself; If “Static” is selected, the Ethernet parameters can be set by user.
Mask | Subnet mask of DVP10MC11T
Gateway | Gateway address of DVP10MC11T

## Slide 7: Setup of Communication Port(4)
9. Return to “Ethernet Setting…” dialog box; select the scanned DVP10MC11T and then click “OK”.
10. Then come back to the main interface of CANopen Builder.

## Slide 8: Network Configuration(1)
Click the icon “ ” on the toolbar to scan the master and slave in the network. The master (DVP10MC11T) and slave (Servo ASDA-A2 ) have been scanned in the following network.

## Slide 9: Configuration & Program Download(1)
2. Then “Axis Configuration” appears, where to conduct the configuration of the axis parameters.
1. After checking that no error exists, double click on “Network” under “Project” and then double click on the icon of A2 servo drive.

## Slide 10: Configuration & Program Download(2)
Explanation of axis parameters:
No. of servo axis
Servo’s name
Axis type:
1. Linear axis
2. Rotary axis
Homing mode: value range:1-35
Homing speed: value range:1-500 rpm
The three parameters are used in the specified occasion. For instance, they can be the speed, acceleration and deceleration of G0 in CNC instruction; when “MC_CamIn” is executed, they are the speed, acceleration and deceleration at which the slave is entering the meshing point; when “MC_GearIn” is executed and, they are the speed, acceleration and deceleration at which slave follows master to move.
Actually, the user-defined parameter is the servo drive parameter. The method of calculating the index and sub-index is as follows.
Index= servo drive parameter (Hex.) + 2000 (Hex.), sub-index= 0
Max. and min. position of the axis limited by software
Servo gear ratio is used to set how many pulses servo drive receives when servo motor rotates for one circle.
The corresponding units that terminal actuator moves when the output end of gear rotates for one circle.
Click “OK” to finish the setting.

## Slide 11: Configuration & Program Download(3)
3. Double click the icon of DVP10MC11T, and then the “Node List Setting” dialog box appears.
5. ASDA-A2 Drive has been allocated into the Node List and then click “OK”.
4. Select ASDA-A2 Drive on the available list; click “>” to allocate it into the master node list and then click “OK” to finish the configuration.

## Slide 12: Motion Control Function Planning(1)
3. After the new program creation is finished, the program name and number are shown under “Program” and the right window is the program editing area.
1. Right click on “Program” on the left project window, select “New Program” in the menu and then “New Program” dialog box appears.
2. The “New Program” dialog box pops up, where to enter the program name, sequence no, view type, author and task type. The CFC language is taken as an example here. After setting is finished, click “OK”.

## Slide 13: Motion Control Function Planning(2)
4. Select the single axis function from the Single-Axis Lib by double clicking the corresponding instruction in the pull-down list and then click on the right program editing area to put the selected instruction.
5. After the instruction is selected, click the right icon ” ” on the toolbar and put the input/ output block to the locations of the input/out pins according to the actual need.
6. Click the pin of input/output block or the instruction and then click the pin of the instruction or input/ output block to be connected and then the connection is finished.

## Slide 14: Motion Control Function Planning(3)
9. Click the icon “ ” on the network toolbar to download the motion control program and configuration information to DVP10MC11T.
7. Double click input/output block to conduct the setting of parameters.
8. Right click on the program editing area and the below menu pops up, where to select “Check All” to check the correctness of the whole program after program editing is completed.

## Slide 15: On-line Monitoring(1)
1. After download is finished, if the CAN and MTL indicators on the panel of DVP10MC11T are in status of being green, it means the network connection is successful and then click the icon “ ” on the toolbar to conduct the monitoring of the program.
D device setting: right click the input block to be set and a menu pops up, where to select “Change Value” and then the value of D10 can be changed.
Bit device setting:
Right click the input block to be set, a menu pops up, where to select “On/Off” and then the status of the bit device can be changed.
2. In status of on-line monitoring, the D device and bit device need be set and the setting method is seen below.

## Slide 16: On-line Monitoring(2)
3. Explanation of Program
a. The servo with the Node ID 1 is started when M0 and M1 are on.
b. The servo starts to move by execution of the velocity instruction when M2 is on.
c. The servo stops moving by execution of the stop instruction when M3 is on.

## Slide 17: Diagnosis of LED and Debugging(1)

## Slide 18: Diagnosis of LED and Debugging(2)

## Slide 19: Diagnosis of LED and Debugging(3)

## Slide 20
Thank you!
Version 1.0 2012.4 PLC
Version 1.1 2012.10 WJSC