## Slide 1
WJ Solution center
2012. Oct. 25
DVP10MC NC function

## Slide 2
Content
1. G-Code Introduction
2. Axis Interpolation
3. Import G-code files
4. G-Code Preview
5. Trace monitoring

## Slide 3: G-Code Instruction
G Code | Function | Format
G0 | Rapid positioning | N_G0 X_Y_Z_A_B_C_P_Q_
G1 | Linear interpolation | N_G1 X_Y_Z_A_B_C_P_Q_ E_E_ F_
G2 | Clockwise Circular interpolation | N_G2 X_Y_Z_A_B_C_P_Q_I_J_T_E_E_F_
 |  | N_G2 X_Y_Z_A_B_C_P_Q_I_K_T_E_E_F_
 |  | N_G2 X_Y_Z_A_B_C_P_Q_J_K_T_E_E_F_
 | helical interpolation | N_G2 X_Y_Z_A_B_C_P_Q_R_T_ E_E_ F_
G3 | Anticlockwise circular | N_G3 X_Y_Z_A_B_C_P_Q_I _J_T_ E_E_F
 |  | N_G3 X_Y_Z_A_B_C_P_Q_I_ K_T_ E_E_F
 |  | N_G3 X_Y_Z_A_B_C_P_Q_J_K_T_ E_ E_F
 | helical interpolation | N_G3 X_Y_Z_A_B_C_P_Q_R_T_ E_ E_ F_
G4 | Dwell instruction | N_G4 K_
G36 | Set/Reset | N_G36 M0 K1
 |  | N_G36 M0 K0
G37 | Status judgment | N_G37 M_ K1
 |  | N_G37 M_ K0
G17 | XY plane selection | N_G17
G18 | ZX plane selection | N_G18
G19 | YZ plane selection | N_G19
G90 | Absolute mode | N_G90
G91 | Relative mode | N_G91

## Slide 4: Axis Interpolation(1)
Max. 8 axis line interpolation
Circular /helical interpolation

## Slide 5: Axis Interpolation(2)
Multi axis interpolation
Pause
Stop
Manual Mode shifting

## Slide 6: Import G-code files
Besides .txt G Code , user can also import DXF format directly which is convert to G Code in CANopenbuider。

## Slide 7: G-Code Preview
User can preview the G-Code in the graphics window，The track in the graphics window will be highlight if the corresponding G-code is selected.
Support G-code graphics enlarge, shrink, shift .

## Slide 8: Trace monitoring
Max. 4 curves can be monitor in each group
Support max. 8 groups trace monitoring , which include y-t and x-y monitoring

## Slide 9: Exercise 1
G01/G02
Try to use G02 to realize the helical interpolation .

## Slide 10
Thank you!
Version 1.0 2012.10 WJSC