## Slide 1
DVP 10MC Flying shear function
WJ Solution center
2012. Aug. 25

## Slide 2: Content
1. Application of Flying Shear Function
2. Feature of Flying Shear Function
3. Technical Parameter of Flying Shear
4. Flying Shear Application Instruction
5. Flying Shear Control Chart

## Slide 3: Introduction of flying shear
Flying shear is the technology of vertically cutting of the material in process of transmission.
The working procedure of the fixed-length cut on material exists in modern sectors such as processing, packaging and etc. For
instance, slitting on the horizontal sealing of the packing bags, punching, printing and so on.

## Slide 4: Feature of Flying Shear
Flying shear is the technology to cut the material in transmission vertically. The slave axis starts to accelerate from the wait position. After its speed is up to the synchronous speed, the follower of the lead screw and material move at the same speed; they are relatively static; the Insync bit is on and the shear axis is triggered to control the shear to do the cutting upward.

## Slide 5: Technical Parameter
Parameter in figure | Description | Name in the instruction
R1 | The radius of master axis, i.e. the radius of the feed roller | MasterRaduis
R2 | The radius of slave axis, i.e. the radius of the corresponding roller of slave axis. By adopting the lead screw, R2= Lead of the lead screw / 2π=S/2π | SlaveRadius
A | The wait position of slave axis. After the flying shear function is started up, slave axis will run to the position automatically. | SlaveWaitPosition
B | The start position of master axis. When master axis reaches this position, slave axis will chase the master axis starting from the wait position to realize the synchronous speed. | MasterStartPosition
C | The corresponding master position when synchronous area starts. | MasterSyncPosition
D | The corresponding slave position when synchronous area starts. | SlaveSyncPosition
E | The corresponding slave position when synchronous area ends. | SlaveEndPosition
L | The cutting length of material | CutLength

## Slide 6: Flying Shear Instruction(1)
Parameter | Explanation
Execute | When “Execute” turns off -> on, the instruction is executed.
MasterRadius | The radius of master axis, i.e. the radius of the feed roller
SlaveRaduis | The radius of slave axis, i.e. the radius of the corresponding roller of slave axis. By adopting the lead screw, R2= Lead of the lead screw / 2π
CutLength | The cutting length of material
MasterStartPosition | The start position of master axis. When master axis reaches this position, slave axis will chase the master axis starting from the wait position to realize the synchronous speed.
MasterSyncPosition | The corresponding master position when synchronous area starts.
SlaveSyncPosition | The corresponding slave position when synchronous area starts.
SlaveEndPosition | The corresponding slave position when synchronous area ends.
SlaveWaitPosition | The wait position of slave axis. After the flying shear function is started up, slave axis will run to the position automatically.
SlaveVelocity | The rotation speed of the terminal actuator of slave axis, the parameter is always positive.(Unit: unit/second)
SlaveAcceleration | The acceleration of the terminal actuator of slave axis, the parameter is always positive.(Unit: unit/second2)
SlaveDeceleration | The deceleration of the terminal actuator of slave axis, the parameter is always positive.(Unit: unit/second2)
FlyingShearID | The number for a group of the flying shear instructions; a group of flying shear parameters use the uniform number. Setting range: 0~7
Done | As the instruction execution is finished, “Done” is on; as “Execute” is off, “Done” is reset.
Error | When any error is detected, "Error" turns on; when "Execute" turns off, "Error" is reset.
ErrorID | Error code. Please refer to section 5.3.
The instruction is used for initializing the radius of master axis and slave axis, the cutting length, synchronous area and etc

## Slide 7: Application Instruction(2)
Parameter name | Explanation
Enable | When “Enable” turns off -> on, the instruction is executed. And then slave axis moves from current position to SlaveWaitPosition.
Start | When "Start” bit is a high level, the shearing will be done continuously; In the continuous shearing, if “Start” bit turns from high to low level, the flying shear relation will be disconnected automatically and slave will stand still at the wait position after the shearing action in current cycle is completed.
MasterAxis | The number of master axis
SlaveAxis | The number of slave axis
FlyingShearID | The number of a group of flying shear instructions; a group of flying shear parameters use the uniform number. Setting range: 0~7
Done | After “Done” is on, it indicates that the already established flying shear relation is disconnected successfully.
Ready | After slave axis reaches the wait position, “Ready” bit is on; when slave axis reaches the synchronous area, “Ready” is reset.
Wait | “Wait” turns on as chase area starts; “Wait” is reset as chase area ends.
Insync | “Insync” turns on as synchronous area starts; “Insync” is reset as synchronous area ends.
Return | “Return” turns on as return area starts; “Return” is reset as return area ends.
Error | When any error is detected, "Error" turns on; when "Execute" turns off, "Error" is reset.
ErrorID | Error code.
The instruction is used for establishing the flying shear relation and specifying the axis number of the master and slave axis according to the application requirement. When the instruction is being executed, its output device can display the zone where the flying shear is. The instruction is also used for disconnection of the flying shear relation.

## Slide 8: Flying Shear Control Chart
Acceleration area: After the flying shear relation is established successfully and when master axis runs to MasterStartPosition, slave axis starts to accelerate from static state and finally slave axis and master keeps the synchronous speed. The process is named as the Acceleration area.
In this area, slave axis and master axis run at the fixed speed ratio (1:1 usually). And the cutting of material occurs in this area.
Return area: After the Sync area finishes, slave axis starts to decelerate and finally slave axis rotates reversely to the SlaveWaitPosition and then stops. The process is named as the Return area.
主轴

## Slide 9
Thank you!
Version 1.0 2012.4 PLC
Version 1.1 2012.9 WJSC